Error Correction
# Overview
The practical asks to write a Java application with a GUI that allows experimentation with Hamming codes. The objective of the experiments is to investigate the trade-off between reliability and information rate. As required, my program generates (2r – 1, 2r – 1 – r, r) linear Hamming codes, encodes data, corrupts it (introduces random errors), and decodes it. By default r takes on values from 2 to 6. After decoding statistics are output reflecting the effectiveness of the code.
On top of these basic requirements, I have implemented two extensions. The maximum value of ‘r’ can be set by the user, thus the codes generated have r starting at 2 and ending at the user defined value. Furthermore, I have implemented and compared Hamming codes to Multi-Dimensional Parity Check (MDPC). This error correcting code offers more reliability in sacrifice of information rate thus allowing a richer evaluation of the trade-off. MDPC can fix up to n/2 errors, where n is the number of dimensions. The sizes of the dimensions reduce the chance of having an error in the data bits and help make the correction process more deterministic.
To run the program simply execute ‘make’ from within the submission directory.
# Definitions
Some definitions for this submission:
weight of an n-bit word is the number of bits set to 1 (aka cardinality or hamming distance from the all-zero n-bit word)
data bits or data part (d) is the part of a codeword that carries the data
parity bits or parity part (p) is the part of a codeword that is attached for error correction
parity generation matrix (X) is the matrix that is used to generate the parity bits for an input word
In is the identity matrix of size n
# Matrices of the Error Correction Codes
This section proves that for each code at most one matrix needs to be stored. That is the common part X of the generator matrix, the parity check matrix, and the syndrome table.
The specification says that we should generate 3 arrays for each Hamming code. Those are a generation matrix, a parity check matrix, and a syndrome table. However, this would take up too much memory for longer Hamming codes (and especially for longer MDPC). The size of the generator matrix for an arbitrary Hamming code is (2r – 1 – r)*(2r – 1) (Ir attached to a matrix of all r-bit words with a weight of 2 or more). The size of the parity check matrix is (2r -1)*r (all r-bit words without the all-zero). Finally, the syndrome table has 2r entries, each consisting of a code word with length 2r –1 and a syndrome of length r (all 2r -1 bit words of weight 1 or 0 and the result of multiplying each by the parity check matrix). Obviously, for larger values of r, 3 matrices of such sizes would take up a lot of memory.
I have therefore opted out of storing all of them and instead I am only keeping the common part X. X is a (2r – 1 – r)*r parity generation matrix (and its smaller than the generator and the parity check matrices). It consists of all r-bit words of weight 2 or more. Since X has the same number of rows as the generator matrix, input data words remain the same length (2r – 1 – r).
Multiplying an input word by X gives the parity of that word which has length r. The codeword is simply the concatenation of the input word and its parity. Resulting in the same word of 2r – 1 bits as multiplying the input word by the generator matrix. Thus, a generator matrix is not needed.
When a codeword is generated, the first 2r – 1 – r bits are the word itself and the latter r bits are the parity bits. Multiplying the codeword by the parity check matrix gives the same as summing the products of the multiplications of (the data part by X) and (the parity part by Ir). That is, for a codeword cw=d+p (concatenation, rather than addition of data part and parity part),
cw*H = d*X+p*Ir. (Since the parity check matrix H consists of all rows of both X and Ir.) The right side of this equation is then d*X + p, as multiplication by any I gives the same word. Therefore, cw*H = d*X + p. Instead of calculating cw*H, it suffice to multiply d by X and then add p. Thus, a parity check matrix is not needed.
A lookup in a syndrome table tells us which bits need to be flipped in order to reconstruct the original codeword. However, there is no practical use of fixing errors in the parity part of a codeword, since, after correction, only the data part is valuable. Thus, we can reduce the size of the default syndrome table by r (amount of entries that have a true bit in their parity part). That is remove the last r entries from the table and the last r bits of each remaining word. We can safely do this as the zero bits do not affect the final product of the multiplication with X. We can also remove the all-zero word. Now, a successful lookup in the syndrome table gives the mask we need to add to the data part in order to restore it to the way it was sent. An unsuccessful lookup means that there is no fixable error in the data bits, in which case the data part is not changed. Now the syndrome table has 2r – 1 – r entries (all 2r bit words with a 1 in their data part) this makes them an I2r – 1 – r . Furthermore, multiplying a word of weight 1 by a matrix gives a product equal to one row in the matrix. The position of the 1 in the word determines the row, the zeros in the word remove the weight of any of the other rows. Therefore, the matrix of the syndromes is the same as X. When a codeword cw is received, the syndrome s is calculated as s = cw*H. Using the equation from above, s = d*X + p. Now, looking up s in X gives the index of the faulty bit in d. Thus, a syndrome table is not needed.
An example syndrome table for r = 3, (7, 4, 3) Hamming code.
error	syndrome
1000 000 / 0100 000 / 0010 000 / 0001 000 / 0000 100 / 0000 010 / 0000 001	011 / 101 / 110 / 111 / 100 / 010 / 001

Clearly, the syndromes form the parity check matrix H for this Hamming code. If we drop the entries that fix errors in the parity of a received codeword, we are left with the parity generation matrix X on the right and I4 on the left. A syndrome’s index in X is the index of the flipped bit.
Multi-Dimensional Parity Check (MDPC) codes, as described in IEEE documentation [1], use a generator matrix to encode and failed dimension marking to correct errors. The generator matrix can be converted to standard form with the basic matrix operations described in the lectures. The algorithm described in the paper essentially multiplies identity matrices and columns of ones. This results in at least one identity matrix within the generator matrix (number depends on the sizes of the dimensions). From a generator matrix in standard form, we can easily extract an identity matrix and have a remaining part X. Now, encoding can happen the same way as Hamming codes – multiplication of input word by X and attaching the result to the input word.
The suggested method for correcting errors is essentially: use the data bits to generate a new parity, compare the calculated parity to the received parity, flip a data bit that would reduce the difference and repeat until either all errors are fixed or it is determined that there are more errors than can be fixed. In practice, the difference between the two parties is the same as their binary addition. Thus, similar to Hamming codes, we calculate expected parity, add it to the received parity, and now we can use X to determine which bit explains most of the changes. Hamming codes try to explain the difference with one row of X (the addition of that row to the sum of the parities must be 0). MDPC takes this further and explains the difference with a sum of multiple rows of X. So, after receiving a codeword cw = d+p (concatenation), we can calculate d*H, add that to p to obtain ps, look for 1 to n/2 rows in X that when summed result in ps. Again, we only need to store the common part X without a generator matrix, a parity check matrix, nor a syndrome table.
# Implementation
I have split my program in two packages. One handles encoding and decoding, providing an interface for those, while the other is the implementation of the GUI.
## Codes
The codes package has 5 classes to represent binary strings, codes, and a couple of operations.
An instance of the ‘Word’ class represents a sequence of binary digits that make up one row, an input word, or an encoded word. I have used Java’s BitSet class for this implementation and defined common operations on binary words as methods. Some of these are addition, multiplication, bit flip, concatenation, Kronecker Multiplication (needed for MDPC).
The abstract class ‘AbstractCode’ defines the basic functionality of every error correcting code. The class also declares a ‘fix’ method which takes a word that needs to be corrected and the sum of the received parity and the calculated parity (this is sum is referred to as the ‘estimatedParity’). The method returns a word after attempting to fix this one (may or may not be successful).
The ‘Hamming’ class is a simple implementation of the Hamming code which provides a constructor that fills the X parity generation matrix and an implementation of the aforementioned ‘fix’ method that looks for the ‘estimatedParity’ in X, if it finds it at index i, it flips the ith index of the given word.
The ‘MDPC’ class contains a constructor, an implementation of the ‘fix’ method and a number of helper methods. One of the helper methods is used to recursively add words of X in an attempt to find which set of indexes sum to ‘estimatedParity’. Note that calculating all possible sums for each codeword has the same complexity as iterating a table that has them all precomputed since the addition (xor) is practically linear. Therefore, I have chosen to reduce space complexity of the algorithm with no effect on the time complexity.
The other helper methods are used when generating the X matrix. I have also written two methods which implement the matrix generation from the paper. They, however, are not used in the program but are simply there for reference. Both of these methods result in a matrix that can be converted to standard. The proof for that is the fact that after encoding, certain bits of the codeword form the data bits (which is used when decoding). Furthermore, generating the matrix involves multiplication of an identity matrix at every stage. This ensures that the matrix can be converted to normal form.
To make a parity generation matrix X without first obtaining any of the other two, I don’t add the identity part until the next iteration of the loop. At each step, Ir is the I matrix that comes next to be added and Ig is the I matrix that would be attached to X to form the generator matrix. Kronecker multiplication takes place as per the algorithm requires and matrices are concatenated. Note that Ir and Ig are not multiplied, therefore X does not have the columns that would form an identity matrix.
Finally, ‘ErrorCorrection’ is the class that contains the static methods that encode and decode messages. These methods are passed a string and an ‘AbstractCode’ (both Hamming and MDPC are children of this class). The methods divide the strings into chunks, apply encoding/decoding respectively and return a new string.
The class also has an utility method ‘zeroExtend’ which adds leading zeros to a message, so that it can be properly divided into chunks.
## UI
The user interface package has 5 classes that represent different layers of my GUI implementation, and one class that performs operations on messages.
The ‘Randomnizer’ class has 3 static methods that generate a binary message of a given length, introduce errors into such a message with a given chance of corruption, and finally invert all the bits of a given message. The first two methods are used when running the experiments, the third one is called when decoding a message with more than 50% chance of error.
As I was writing my GUI, the code became longer and longer, new variables got introduced and more positioning code was added. So, I decided to split the code of the interface into five classes that are bound by inheritance. Dividing the code amongst files was necessary, but all the methods needed access to the variables of the Jframe. Having them inherit from one another gives the methods all the necessary access without having to pass around a Jframe object, and makes the code cleaner and easier to read. The inheritance relationships are as follows: Layer 1 extends Jframe, Layer 2 extends Layer 1, … Layer 5 extends Layer 4. Layer 5 is the runnable class with a main method that creates a Jframe object and calls the appropriate methods. Each layer has a name that reflects its purpose. Layer 1 holds all the variables declarations. Layer 2 defines how input is parsed from the user. Layer 3 defines all the components on the main Jframe. Layer 4 runs all the experiments and writes the results in components of the Jframe. Layer 5 defines how the components react to different user inputs. As can be seen, each layer requires functionality from the ones below it, making this way of organization very useful.
Lastly, here are some notes on the overall user interface.
The components are put inside tabs. There is a main tab that allows configurations on how an experiment is run, the ‘GO’ button and two tables the present statistics (more on those below). When the ‘GO’ button is pressed, the experiment as described in the practical specification, is run. By default, 100 runs are performed, each message has a length of 500 bits, the probability with which errors are introduced is 5%, the probability of 1 (true bit) in the generated string is 50% (leaving also 50% for 0, false bit). The ‘Max r’ field sets the maximum r for which encoding should be done. By default, that is 6 and it runs experiments with Hamming of r = 2, 3, 4, 5, 6. Setting a higher value will expand this list. The dimensions for the MDPC codes are the values of r. For each value of r, a new tab is created that shows the results of runs. In each tab r = k, there are the Hamming code (2k – 1, 2k – 1 – k, 3) and MDPC with k-1 dimensions with values from 2 to k. This means that for larger values of Max r, the codes will become exponentially longer and will take more time to run. The reduce the wait time for some tests, I have added the ‘Do MDPC?’ check box. If that box is not selected, MDPC will not be performed, allowing experimentation with longer Hamming codes, without the incredible slowness of MDPC.
There is a ‘Custom r’ tab which can be used to experiment with larger codes without running through all the smaller codes. The values entered in the ‘r = ‘ field are used as dimension lengths of MDPC. The number of values gives the ‘r’ of the Hamming code. Note that a dimension of length 1 does not change he MDPC code, so one can add multiple ones to increase the Hamming code while keeping the same MDPC. So, entering “3,1,5,2” will make a Hamming code with r=4, and a 4-Dimensional Parity Check code of which the second dimension has no effect on the code (and is therefore the same as a 3-DPC with dimensions (3, 5, 2)).
Pressing Enter while editing the r values in the custom tab will run the experiment only for the custom tab. Pressing Enter while editing the number of runs to perform will run the experiment for all r form 2 to max r but NOT for the custom tab. Pressing Enter while editing the message will run the full experiment with only that message.
In the default case when ‘GO’ is pressed, first all r from 2 to max r get run and then the custom tab gets run. That is, a message is generated, it is passed to all tabs with ‘r=?’, then the next message is generated, repeating for the number of runs. After that the same is performed with the custom tab. This is why after pressing ‘GO’ the message displayed is not the one in the ‘r=?’ tabs but only matches the one in the custom tab.
# Statistics
To generate statistics I am using Apache’s math3 Java library which has a built-in one way ANOVA functionality. All the required statistical information is presented in two tables in the main tab. The first one contains the analysis over all the Hamming codes. The second one contains the analysis of the combined Hamming codes vs the combined MDPC codes. Running the experiment multiple times consistently yield significant results with a significance level between 1 and 3 %.
The ANOVA thus proves that the difference between the distances (distance between original word and decoded word) is significant. Looking at the tables in the other tabs, it can be seen that as the length of the code increases, the number of uncorrectable errors also increases. As can be seen from the short tables in the tabs, the longer the Hamming code, the more likely it is to get an error in the data bits. In a channel with lower probability of error, longer Hamming codes are usable and will allow higher information rate. On a more noisy channel, a shorter Hamming code is preferred but that will limit performance.
An alternative is to use MDPC codes for better error handling on a noisy channel, while maintaining a relatively good bandwidth. As the number of dimensions of a MDPC code grows, the information rate falls drastically. The information rate for each dimension of length k is (k – 1)/k. The total information rate is the product of these ratios. So, for a (2,3,4,5) MDPC, the information rate is (2-1)*(3-1)*(4-1)*(5-1)/(2*3*4*5) = 2*3*4/(2*3*4*5) = 1/5 = 0.2. Much less than Hamming codes but much better at fixing errors.
The ANOVA analysis between Hamming and MDPC proves that there is a statistically significant difference between the two. Observing the long tables in the tabs shows that MDPCs are better at correcting errors.
# Conclusion
Overall, my submission achieves all required basic functionality, as well as a number of small GUI extensions, an optimized way of working with code matrices, and the implementation of another error correction code used for comparison in the analysis. I found the assignment very fascinating and I would have loved to implement the following features in addition: a parity generation matrix X that gets generated on the go (seems easy enough for Hamming, but not so much for MDPC); an implementation of another error correction code (a circular code for example) to analyse that performance as well; multiple small GUI features that would enhance the user experience with the interface.
# References
While I only used material from the first piece of referenced work, I did look at others when considering which code to implement and the ones on Low Density Parity Check were quite interesting.
1. Ludek Dudacek, Ivo Vertat
Multi-Dimensional Parity Check codes with short block lengths
https://doi.org/10.1109/TELFOR.2016.7818772
2. DJC MacKay and RM Neal
Near Shannon limit performance of low density parity check codes
http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=533358&tag=1
3. RG Gallager
Low-Density Parity-Check codes
http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=1057683